## Slide 1
Mark Heggli, Meteorologist/Hydrologist
Expert Real-time Hydrology Information Systems
Innovative Hydrology, Inc.
Consultant to the World Bank
HP-II Workshop on Real-time Hydrological Information Systems
Module 3: Site Selection & Security

## Slide 2
Examples that refer to products are intended for illustrative purposes only, and do not imply an endorsement or recommendation of any particular product

## Slide 3: Site Selection and Security Consideration
Site selection
  Define the Site Purpose
  Site Survey/ Field Visit
Security considerations for all sites

## Slide 4: Define The Site Purpose
Establish the purpose of the site
  What are you trying to measure?
    Water Level
    Discharge
    Water Temperature
    Water Quality
    Rainfall
    Other
  How crucial is the data?
    Logging needs
    Frequency of Data Collection
Consideration of future needs
  Additional sensors, additional telemetry

## Slide 5: Site Survey/Field Visit
Why is it important to complete a site survey?
  Ease and safe accessibility
  Understand the characteristics of the area being measured
    Understanding the characteristics will help in the decision making of proper equipment to make accurate measurements
    A mismatch between local conditions and appropriate technology can result in:
      Poor quality of data
      High maintenance requirements for both field and office procedures

## Slide 6: Accessibility and Safety
Safe access to site
  Road
  Path
  Boat
  Aircraft
Minimization of risk during install, ongoing operation and maintenance
  Personnel, sub-contractors, public

## Slide 7: Water Level and Discharge Sites
Stream characteristics
  Control
  Upstream and downstream considerations
  Contained and subterranean flow
  Streambed and banks
  Gauging sections

## Slide 8: Control
What to look for in a control?
  Control needs to be stable and sensitive
    Minimum change in discharge with minimum change in stage
    Cease to flow point should not be affected by sedimentation or weed growth
  Try to find a site with an existing natural control
Types of Control
  Natural control
  Man made control

## Slide 9: Upstream and Downstream Considerations
Straight section of stream
  According to the WMO, the general course of the stream is straight for about 10 times the stream width, upstream and downstream from the gauge site if the control is a river reach (channel control).
  Approach velocities are evenly distributed
  Avoid cross-section where sediment deposition/scour is prevalent
Downstream Effects
  Evaluate downstream effects (tidal effects, water shortages, future civil works/dams)

## Slide 10: Contained and Subterranean Flow
Contained Flow
  Section needs to contain all flow including maximum flood flow
  No possibility of over bank or side channel flow
Subterranean Flow
  Evaluation should include possibility of subterranean upstream, causing bypassing of flow (prevalent in underground mining areas)

## Slide 11: Stable Stream Bed and Banks
Stable Stream Bed
  Minimal infill or scour
Stable Stream Banks
  Avoid locations with bank scour or erosion

## Slide 12: Gauging Sections
Gauging Sections
  Feasibility
    Low flow wading
    Boat measurement
    Unmanned cableways

## Slide 13: Rainfall Site Selection
Obstruction
Non windy area
Not on top of a mountain
Flat surface, no slopes
Height of gauge
  1 m is standard according to WMO
  Wind velocities increase with height
  High enough to prevent splashing from the ground

## Slide 14: Location of Instrumentation
Power
  AC
  DC- Generator or Battery
    Solar needs a clear access to sunlight
Telemetry
  Landline
  GPRS/GSM Coverage
  Radio Link
  Satellite Access
Housing of Equipment
  Location of instrumentation must be above maximum flood

## Slide 15: Security Considerations
All Sites
  Locks
  Fencing
  Disguise

## Slide 16: Suggestions
Rarely will an ideal site be found for a gauging station
  Judgment must be exercised in choosing between adequate sites, each of which may have some shortcomings
Often adverse conditions may exist at all possible sites for installing a required gauging station and a poor site must be accepted
  For example, all streams in a given region may have unstable beds and banks, which result in continually changing stage-discharge relations

## Slide 17: QUIZ
What is wrong with this location for a precipitation gauge?

## Slide 18: QUIZ
Is this a good location for a gauging site?

## Slide 19: QUIZ
a. High maintenance requirements
b. Good equipment can fix poor choice in location
c. Poor quality of data



Poor choice in site selection can result in what?

## Slide 20: End of Module 3